## Slide 1: Collision-free positioning of optical fibers
From MOONs to Sloan
25.01.2018

## Slide 2: Program
From MOONS to Sloan : reminder
Presentation of the jobs done and ongoing
Recap
To do list

## Slide 3: From MOONS to Sloan reminder
Specific motor arrangement
  500 motors
  Void rectangle at the center
From 1 to 3 fibers available
  Only some motors own an IR fiber
  The target is not set on the middle
  of the ferule anymore

## Slide 4: Parameter file
Purpose : group all parameters (dimensions, decentralized navigation function, simulation constants) in one text file.

## Slide 5: Parameter file
Before

## Slide 6: Parameter file
Before
After

## Slide 7: Circles program
Purpose : creating a program spawning the hexagonal shape of the positioner ensemble, containing positions and fiber properties in arrays to be used everywhere else in the software.

## Slide 8: Circles program
Operation :
  Creates a circle at position (0,0)
  Surrounds this circles with 6 circles
  Repeat the process until the wished number

## Slide 9: Circle program flexibility
Addition of Empty actuators

## Slide 10: Circle program flexibility
Addition of Fiducial actuators

## Slide 11
Addition of a layer of actuators
Circle program flexibility

## Slide 12
Addition separation length between actuators
Circle program flexibility

## Slide 13: Circles program
Advantages :
  No need of the cfg file for the motor coordinates (very long for the entire telescope)
  Every information concerning positions and fibers automatically generated
  Easy visualization
  Flexibility to several modifications
Disadvantages :
  Hardcoding necessary for certain modifications
  Rectangle at the center is programmed to be filled with motors unable to set any target

## Slide 14: Circles program

## Slide 15: Set_target update for fibers
Purpose : moving the motor to a close position of the center of the ferule, under the wished fiber

## Slide 16: Set_target update for fibers
Possibilities :
  Displacing the position of the target depending on the choice of the fiber
  Changing the coordinates of the wished position for each motor, depending on the wished fiber
  Moving each motors to the target (under the center), and then ask a small displacement to move the fiber under the target

## Slide 17: Set_target update for fibers
Possibilities :
  Displacing the position of the target depending on the choice of the fiber -> adds confusion and problems for visualization.
  Changing the coordinates of the wished position for each motor, depending on the wished fiber -> the position of the fiber depends on the former final angle values
  Moving each motors to the target (under the center), and then ask a small displacement to move the fiber under the target -> clash and DNF problems

## Slide 18: Set_target update for fibers
  2. Changing the coordinates of the wished position for each motor, depending on the wished fiber -> the position of the fiber depends on the former final angle values

## Slide 19: Set_target update for fibers
No correction
With correction
With correction x4

## Slide 20: Target generator
Purpose : having a bank of target files to test the software when ready
5 types :
  Random
  Random with normal distribution on the center
  Focused on a random place
  Focused on a random place with normal distribution
  Homogeneous (looks like former target files)
Plots available

## Slide 21: Target generator
Random
Random normal
Homogeneous
Focus normal
Focus

## Slide 22: Fiber attribution
Purpose : set a motor to a target only if this motor contains the necessary fiber

## Slide 23: Fiber attribution
Purpose : set a positioner to a target only if this motor contains the necessary fiber
Operation :
  New column in the target file, indicating which fiber to choose
R positioner coord. | Theta positioner coord. | R target coord. | Theta target coord. | Arg 1 parity | Arg 2 parity | Priority positioner | Fiber
Before
After

## Slide 24: Fiber attribution
Purpose : set a positioner to a target only if this motor contains the necessary fiber
Operation :
  New column in the target file, indicating which fiber to choose
  Program generating random fiber attribution to any former target file
  If a positioner is “empty” (empty rectangle for Sloan) or a fiducial, target is not set
  If the target needs IR fiber, but the proposed positioner only has visible and calibration, target is not set
  If the target needs IR fiber, and the proposed positioner owns an IR fiber, nothing changes
  If the target needs visible or calibration fiber, nothing changes

## Slide 25: Fiber attribution
Operation :
  New column in the target file, indicating which fiber to choose
  Program generating random fiber attribution to any former target file
  If a positioner is “empty” (empty rectangle for Sloan) or a fiducial, target not set
  If the target needs IR fiber, but the proposed motor only has visible and calibration, target not set
  If the target needs IR fiber, and the proposed motor owns an IR fiber, nothing changes
  If the target needs visible or calibration fiber, nothing changes

## Slide 26: Architecture : former

## Slide 28: Recap
Parameter script and file managing parameters throughout the entire program.
Sloan positioner ensemble structure has to be updated following January 2018’s modifications
Set_target update to correct or continue
Target generator allow the test of the program when ready
Fiber attribution working: a visible-calibration positioner can not be set on a IR target. Fake (“empty”) and fiducial can not be set either.

## Slide 29: To do
Add fiducials in the DNF (to prevent positioner-fiducial clashes)
Update the positioner structure to January 2018’s modifications
Correct the update of the Set_target function
Former to do list :
  Improve algorithm to increase convergence rate
  Improve prioritization

## Slide 30: Thanks!
Any question/request?

## Slide 31: Job Done
Parameter program
Circles program
Fiber attribution
Target generator to test the program
New architecture